## Slide 2
Overview
Introduction (Fiber Optics Focus ) 01
Networks (LAN, WAN , MAN, PAN) 02
Network Topology (Bus, Star, Ring, etc.) 03
Network Devices (Router, Switch) 04
IP Addressing (IPv4,IPv6, subnetting) 05
OSI Layer 06
Common Networking Protocols 07
Cable Structuring & Standard 08
Wi-Fi Standard (802.11 a/b/g,802.11n, 802.11ac,802.11ax) 09
Network Troubleshooting Tools 10
Network Security (Firewall, Encryption, VLAN, VPN, IPS/ IDS) 11
Understanding Network terms: 12
(Bandwidth, Speed, Throughput, Latency )
Core Networking 13
LABs ( Hands-on Practical ) 14
Questions & Test 15

## Slide 3
  Network Basics for Field Service Technicians (Fiber Optic Focus)
  Field Service Technicians in the telecommunications industry, especially those working with fiber optic networks, need to understand key networking principles to diagnose issues, install and maintain systems, and ensure reliable service. Below are the core network concepts and fiber-specific knowledge that every field technician should be familiar with:
  1. What is a Network?
  A network is a group of two or more devices (computers, routers, printers, etc.) connected to share data and resources, such as files, printers, or internet access.
Introduction to Network
Technology

## Slide 4
Types of Networks
• Local Area Network (LAN): A network confined to a small geographical area, such as a single building or campus.
• Wide Area Network (WAN): A network that spans a large geographical area, like connecting different cities or countries.
• Metropolitan Area Network (MAN): A network that covers a larger area than a LAN but smaller than a WAN, like a city.
• Personal Area Network (PAN): A small network typically around a single person, often used for connecting devices like smartphones, tablets, and laptops.
Network Topologies
The topology defines the physical or logical layout of the network. Common topologies include:
• Bus Topology: All devices are connected to a single cable (the bus).
• Star Topology: Devices are connected to a central hub or switch.
• Ring Topology: Devices form a closed loop, where data travels in one direction.
• Mesh Topology: Every device is connected to every other device.
• Hybrid Topology: A combination of two or more topologies.
Network Types & Topology
Technology

## Slide 5
4. Network Devices
Common networking devices include:
Router: Routes data between different networks, typically between a local network and the internet.
Switch: Operates within a LAN and forwards data to specific devices based on MAC addresses.
Hub: An older device that broadcasts data to all connected devices, unlike switches, which direct it to specific ones.
Access Point (AP): A device that allows wireless devices to connect to the network.
Modem: Converts digital data from your device into analog signals that can be transmitted over telephone lines or coaxial cables.
Firewall: A security device that monitors and controls incoming and outgoing network traffic based on security rules.
Introduction to Network
Technology

## Slide 6
5. IP Addressing
Each device on a network is identified by a unique IP address. There are two versions:
IPv4: Uses 32-bit addresses (e.g., 192.168.1.1).
IPv6: Uses 128-bit addresses (e.g., 2001:0db8:85a3:0000:0000:8a2e:0370:7334).
IP addresses are typically assigned via:
Static IP: Manually configured and remains constant.
Dynamic IP: Assigned automatically by a DHCP server.
6. Subnetting
Subnetting is the process of dividing a large network into smaller sub-networks. It involves:
Dividing an IP address into a network and host portion.
Using a subnet mask (e.g., 255.255.255.0) to determine the range of IP addresses available in a subnet.
IP Address & Subnet
Technology

## Slide 7
7. OSI Model (Open Systems Interconnection)
The OSI model is a conceptual framework that standardizes the functions of a network into 7 layers:
Physical Layer: Transmits raw data over the physical medium (cables, wireless).
Data Link Layer: Manages device-to-device communication, error detection, and flow control (e.g., Ethernet).
Network Layer: Handles routing and addressing (e.g., IP).
Transport Layer: Ensures reliable data transfer (e.g., TCP/UDP).
Session Layer: Manages sessions and controls dialogues between computers.
Presentation Layer: Ensures data is in a readable format (e.g., encryption, compression).
Application Layer: Where user-level applications and network services (e.g., HTTP, FTP) interact.
OSI Model
Technology

## Slide 8
8. Common Networking Protocols
TCP/IP (Transmission Control Protocol/Internet Protocol): The suite of protocols used for internet and local networking.
HTTP/HTTPS (Hypertext Transfer Protocol/Secure): Used for web communication.
FTP (File Transfer Protocol): Used for transferring files.
DNS (Domain Name System): Resolves domain names (like www.example.com) to IP addresses.
DHCP (Dynamic Host Configuration Protocol): Automatically assigns IP addresses to devices on a network.
SMTP (Simple Mail Transfer Protocol): Used for email transmission.
SNMP (Simple Network Management Protocol): Used for network device management and monitoring.
Common Network Protocols
Technology

## Slide 9
9. Cabling Standards
The physical medium through which data is transmitted in a network is typically:
Twisted Pair Cables (Cat5e, Cat6, Cat6a, Cat7): Used in Ethernet networks. Cat6 is the most common for gigabit speeds.
Fiber Optic Cables: Used for high-speed, long-distance transmission. Types include single-mode and multi-mode fiber.
Coaxial Cables: Common in older networking systems and broadband connections.
10. Wi-Fi Standards
Wi-Fi is based on the IEEE 802.11 standards. The main versions include:
802.11a/b/g: Older standards, now largely obsolete.
802.11n: Introduced MIMO (Multiple Input Multiple Output) for faster speeds.
802.11ac: Provides gigabit speeds, and operates on the 5 GHz band.
802.11ax (Wi-Fi 6): The latest, offering higher throughput, improved efficiency, and better support for high-density environments.
Cabling & Wi-Fi Standards
Technology

## Slide 10
11. Network Troubleshooting Tools
Ping: Tests connectivity between devices.
Traceroute: Traces the path data takes across the network to a destination.
nslookup: Queries DNS servers for domain name resolution.
ipconfig/ifconfig: Displays network configuration details on Windows/Linux, respectively.
Wireshark: A network packet analyzer used for capturing and inspecting network traffic.
Netstat: Displays active network connections and listening ports.
12. Security Considerations
Network security is critical to protect data and prevent unauthorized access:
Firewalls: Control traffic based on rules.
Encryption: Protects data privacy (e.g., SSL/TLS for websites).
VLANs (Virtual LANs): Segregate network traffic for better security and performance.
VPN (Virtual Private Network): Encrypts traffic for secure remote access.
IDS/IPS (Intrusion Detection/Prevention Systems): Monitors network traffic for suspicious activity.
Network Troubleshooting Tools
Technology

## Slide 11
13. Understanding Bandwidth and Speed
Bandwidth: Refers to the capacity of the fiber optic link, i.e., how much data can be transmitted in a given amount of time (measured in bits per second).
Latency: The time it takes for data to travel from one point to another on the network. Fiber optic networks typically have low latency compared to copper or wireless connections.
Data Throughput: The actual speed at which data is transmitted across the network. This can be affected by factors like network congestion, distance, and equipment performance.
Bandwidth & Speed
Technology

## Slide 12
14. Functions of the Core Network
Routing and Switching: The core network is responsible for directing data packets from source to destination. This involves finding the best path, dealing with congestion, and ensuring efficient traffic management.
Traffic Management and Quality of Service (QoS): Core networks must prioritize traffic based on the type of service (e.g., voice, video, or data). For example, real-time communication (like VoIP or video calls) requires high priority to ensure quality and low latency.
Addressing and Network Management: The core network handles the allocation of IP addresses and network resources. This includes services like DHCP (Dynamic Host Configuration Protocol) for assigning IP addresses and DNS (Domain Name System) for resolving domain names.
Connection to Edge Networks: The core network connects the network's edge (where end devices connect, such as base stations, customer premises equipment, etc.) to the broader internet and other external networks.
Security and Encryption: Security protocols in the core network ensure that communication is protected. This includes encryption of data, authentication, and access control.
Functions of the Core Network
Technology

## Slide 13
THANK YOU